## Slide 1: GPU accelerated Localization and Mapping (SLAM)
Nischal K N
University of Pennsylvania
CIS 565 – Final Project
Final Project Presentation

## Slide 2: SLAM
SLAM – Simultaneous localization and Mapping
Solve two problems at once
  Find out where you are in the current map
  Update the map with what new information you know about it

## Slide 3: Data Source - LiDAR
270 degrees horizontal field of view
Step 0
Step 1079
Step 1
Step k
Step k+1
Angular resolution 0.25 degrees
Range
10m
Hokuyo UST-10LX

## Slide 4
Scan 1
x
World reference
frame
y
Car reference
frame
A1
y
x

## Slide 5
Scan 2
x
World reference
frame
y

## Slide 6
Scan 2
x
World reference
frame
y

## Slide 7
Scan 2
x
World reference
frame
y

## Slide 8
Scan 2
x
World reference
frame
y

## Slide 9: Demo

## Slide 10: Operation on CPU vs GPU
Chart: 
| CPU (ms) | GPU (ms)
copyLocalToGlobal | 7.96 | 2.34
convertToCartesian | 0.042 | 0.007
convertToCells | 0.014 | 0.003
createLmap | 0.378 | 0.128
generateParticles | 50.31 | 12.743
mapCorrelation | 11.155 | 2.243
calculateCDF | 0.003 | 0.241
resampleParticles | 0.295 | 0.098

## Slide 11: Execution Time vs Particles
Chart: No of Particles
| 100 | 500 | 1000 | 2000 | 5000 | 7000
CPU | 33.334 | 68.173 | 125.335 | 245.338 | 589.797 | 818.826
GPU | 28.031 | 28.532 | 32.871 | 35.218 | 49.142 | 72.142
GPU(zero copy) | 27.42 | 28.312 | 32.423 | 34.376 | 48.423 | 70.423

## Slide 12: Performance Comparison
With cudaMemCpy
Zero copy access
Update Rate: 25.231 Hz
Update Rate: 26.012 Hz

## Slide 13: Operating Frequency
CPU
2320500 kHz
2014500 kHz
1734000 kHz
1428000 kHz
1122000 kHz
GPU
852000 kHz
708000 kHz
612000 kHz
396000 kHz
180000 kHz
Three kernels evaluated
Particle generation and scan orientation
Calculation of Correlation Scores
Copy of Local Map to Global Map

## Slide 14: Operating Frequency

## Slide 15: Limitation – High Particle Count